| Parameters of C4000 |
| --- |
| Physical characteristics Dimensions: 153*75*29 mm Weight: 300 g (with battery) Screen: 4” TFT-LCD, 160K colors. 480X800(WVGA ) Touch panel: capacitive Backlight: LED backlight Battery: rechargeable li-ion polymer battery (3.7 V/3,200 mAh) Expansion slots: SIM/SAM, Micro SD (TF) card Indicator: LED Input method: touch input and keyboard input Audio: 0.5 watt Operating system Android 4.1 Programming environment Language: Java Tool: Eclipse Environmental Operating temperature: 10 ℃ ~ 50 ℃ Storage temperature: -40 ℃ ~ 70 ℃ Humidity: 5% RH ~ 95% RH (non-condensing) Dropping survive: 1.2-meter drop test on six sides (concrete floor, under operating temp) Rolling survive: 1,000 times, 0.5 meter, rolling by six contact surfaces Environmental sealing: IP64 (not included FPS part) Performance CPU: COTEX-A9 1GHz Dual Core Memory: 1GB RAM Storage: 4GB FLASH; MicroSD/TF card Expansion Memory: support maximum 32GB Interfaces: Micro USB,UART |  | LF/HF/UHF (Optional) Operating frequency: 125kHz,13.56 MHz, 900MHz Protocol: ISO11784/5, ISO14443A/B, 15693, ISO18000-6C (optional) Read/write range up to: 2-8 cm (LF/HF), 50-350CM (UHF) Fingerprint Sensor type: capacitive type Function: fingerprint enrollment, process, acquisition, compare, delete etc. Performance: FRR < 0.1%; FAR < 0.001% Math time（1:1）: < 0.1 sec（1:N）: < 0.5 sec 1D laser scanner (Optional) Brand: Symbol SE955(laser) Types: UPC/EAN, Code128, Code39, Code93, Code11, Interleaved 2 of 5, Discrete 2 of 5, Chinese 2 of 5, Codabar, MSI, RSS Brand: Symbol SE655(CCD) Types: UPC/EAN, Bookland EAN, Code 128, Code 39, Code 93, Code 11, Interleaved 2 of 5, Discrete 2 of 5, Chinese 2 of 5, Matrix 2 of 5, Inverse 1D, MSI, GS1 DataBar 2D scan engine (Optional) Brand: Symbol SE4500 Types: 1D: all major codes; 2D: PDF417, MicroPDF417, Composite, RSS, TLC-39, Datamatrix, QR code, Micro QR code, Aztec, MaxiCode; Postal Codes: US PostNet, US Planet, UK Postal, Australian Postal, Japan Postal Dutch Postal (KIX) Postal Codes: US PostNet, US Planet, UK Postal, Australian Postal, Japan Postal Dutch Postal (KIX) |  | Wireless LAN WiFi: IEEE 802.11 b/g/n Wireless WAN (Optional) Network (WWAN): GPRS/GSM 900/1800 MHz; 850/900/1800/1900 MHz (optional) 3G/W-CDMA (optional) Wireless PAN Bluetooth: Class V2.1+EDR, 3-5 M PSAM (Optional) Baud rate: 9600, 19200, 38400, 43000, 56000, 57600, 115200 SAM slots: maximum 2 GPS (Optional) GPS, A-GPS Camera (Optional) Samsung 5.0 mega pixels, Autofocus, Flash Accessories Standard: battery, charger/adapter, data cables, stylus, hand strap, snap-on adapter. Optional: cradle, thermal printer, pistol grip Refer to C4000 Accessories Appendix |